## Slide 1
NSCC: Network-aware Smart Congestion Control
A Deep Dive into Datacenter Congestion Control for Multi-Path Fabrics
Based on UET / SMaRTT-REPS | htsim2 Simulator Implementation

## Slide 2
Lecture Outline
1. The Problem: Why Datacenter CC is Hard
2. NSCC Mental Model: Two Signals, Four Quadrants
3. Window Management: Increase & Decrease Laws
4. Delay Measurement & Filtering
5. Quick-Adapt: The Emergency Brake
6. Packet Spraying & Multi-Path Load Balancing
7. Parameter Scaling Across Network Speeds
8. SLEEK Loss Recovery
9. NSCC vs TCP Cubic vs DCQCN
10. Simulation Results & Validation
11. Key Takeaways & Design Philosophy

## Slide 3
1. The Problem
Why traditional congestion control breaks in modern datacenters

## Slide 4
The Datacenter Challenge
Multi-path fabrics (ECMP, spray)
  Packets take different paths → routine reordering
  TCP's 3-DupACK loss detection fails
Shallow buffers (10-50 us)
  Switch memory is expensive silicon
  Millisecond-scale TCP RTOs are far too slow
Microsecond-scale RTTs (5-20 us)
  BDP ≈ 150 KB at 100 Gbps, 12 us
  Must react in ~1 RTT, not 100s of ms
Incast: 32 senders → 1 receiver
  Queue builds in < 1 us
  Need emergency brake, not gentle backoff
Protocol Comparison
Feature TCP Cubic DCQCN NSCC
─────────────── ─────────── ─────────── ───────────
Signal Loss ECN+Rate Delay+ECN
Multi-path No No Native
Decrease 30% cut Rate steps Proportional
Recovery 3-DupACK Go-back-N SLEEK probe
Response time ~RTT 55 us timer Per-ACK
Incast handling Poor Timer-based Quick-Adapt

## Slide 5
2. NSCC Core Algorithm
Two signals × two states = four quadrants

## Slide 6
NSCC's Two Congestion Signals
Signal 1: Queue Delay
qdelay = raw_RTT - base_RTT
  Measures excess time in switch queues
  Continuous signal: how far from target?
  Compared against target_Qdelay
Signal 2: ECN / Trimming
Switches mark packets when queue > threshold
  Trimming: payload stripped, header forwarded
  Binary signal: was the network stressed?
  Receiver echoes back to sender in ACK
Key Insight
Delay tells you HOW MUCH
the network is congested
ECN/Trim tells you WHERE
the congestion is happening
Together they give magnitude + location
→ proportional response, not binary

## Slide 7
The Four Quadrants
No Trim (ACK) Trim (NACK / ECN)
Delay < Target
Delay ≥ Target
Q1: Proportional Increase
Network has spare capacity inc += α × acked × (target − delay) Bigger gap → faster ramp
Q3: NOOP (Path Switch)
Trim but delay is low? Wrong path, not congestion No CWND change Steer to different path
Q0: Fair Increase
Queues building, but no trim yet inc += fi × acked (fi = 5 × MSS × scale) Conservative, ensures fairness
Q2: Multiplicative Decrease
Active congestion confirmed cwnd × (1 − γ × (delay−target)/delay) γ = 0.8, max 50% cut Rate-limited: once per RTT

## Slide 8
3. Window Management
Four increase mechanisms, one proportional decrease

## Slide 9
Four Increase Mechanisms (Fastest → Slowest)
1
Fast Increase
cwnd += acked × 0.25
When: delay < 1 μs
Cold-start bootstrap
~25% cwnd growth per RTT
2
Proportional Increase
inc += α × acked × (target − delay)
When: Q1: no trim, delay < target
Capacity seeking
Scales with headroom to target
3
Fair Increase
inc += 5 × MSS × acked
When: Q0: no trim, delay ≥ target
Fair convergence
Constant per-ACK, like Reno's AI
4
Eta (η) Liveness
cwnd += 0.15 × MSS
When: Every RTT (periodic)
Prevent starvation
Tiny floor: always make progress

## Slide 10
Proportional Decrease & Fulfill Adjustment
Multiplicative Decrease (Q2)
cwnd × max(1 − γ × (delay−target)/delay, 0.5)
γ = 0.8 — aggressive but bounded
Never cuts more than 50% in one step
Rate-limited: at most once per base_RTT
Uses avg_delay (EWMA), not instantaneous
Proportional to severity:
Delay barely above target → small cut
Delay 2× target → large cut
At equilibrium: (delay−target)/delay → 0
Fulfill Adjustment (Batched)
Increases aren't applied per-ACK.
They accumulate in _inc_bytes, then:
cwnd += _inc_bytes / _cwnd + η
Triggered when:
Byte trigger: received > 8 × MTU
OR time trigger: elapsed > 1 RTT
Division by cwnd is key:
Small window → large per-byte increase
Large window → small per-byte increase
→ Flows converge to equal share

## Slide 11
4. Delay Measurement & Filtering
The thermometer that drives every decision

## Slide 12
Measuring Queue Delay
Base RTT: The Zero Point
Minimum RTT observed by the flow
Represents pure propagation delay
Monotonic decrease refinement:
if raw_rtt < base_rtt: base_rtt = raw_rtt
Queue Delay Extraction
qdelay = raw_rtt − base_rtt
Always ≥ 0 (by construction)
This is what NSCC reacts to
EWMA Delay Filter
avg = (1−α)×avg + α×sample
α = 0.0125 (1.25%)
~80 ACK samples to 63% convergence
Separates per-packet noise from trend
Three Special Cases:
No ECN + high delay:
  → Discount to base_rtt × 0.25
  (avoid false positives from path noise)
ECN marked:
  → Trust full sample (confirmed signal)
Low delay:
  → Trust sample (good news is real)

## Slide 13
Target Delay: The Decision Boundary
How target_Qdelay is determined:
Priority 1: CLI flag -target_q_delay (explicit override)
Priority 2: 0.75 × network_rtt (with trimming enabled)
Priority 3: 1.0 × network_rtt (without trimming)
Why target_Qdelay matters:
Below target → Q1: proportional increase (seek more bandwidth)
Above target → Q0: fair increase only (be conservative)
Above target + trim → Q2: decrease (back off)
It's the equilibrium point — at target, increases taper to zero
and decreases are minimal. The system is in balance.

## Slide 14
5. Quick-Adapt
The emergency brake for incast and topology changes

## Slide 15
Quick-Adapt Mechanism
The Problem
32:1 incast: queue fills in < 1 μs
Iterative multiplicative decrease
  takes 5-10 RTTs to converge
By then, buffers overflow → packet loss
The Solution: Measure & Clamp
Track achieved_bytes per RTT window
If achieved << maxwnd → window is inflated
Action: cwnd = achieved_bytes
One-shot: converge in 1 RTT, not 10
Three Trigger Conditions (ALL required)
① Time window expired
now > qa_endtime (1 RTT + target_Qdelay)
② Congestion signal present
NACK received OR loss OR
delay > 4 × target_Qdelay
③ The Gate Check (qa_gate)
achieved_bytes < maxwnd >> qa_gate
qa_gate=1 → threshold=maxwnd/2 (easy)
qa_gate=2 → threshold=maxwnd/4 (default)
qa_gate=3 → threshold=maxwnd/8 (strict)

## Slide 16
6. Packet Spraying & Load Balancing
Steer first, throttle second

## Slide 17
Multi-Path Load Balancing
Path Selection Strategies
Oblivious: Round-robin with XOR permutation
Bitmap: Penalty score per path, skip bad paths
REPS: Recycle good paths, remove bad ones
Mixed: Hybrid approach
Feedback Integration
PATH_ECN → penalize path (congested)
PATH_NACK → heavy penalty (fabric trim)
PATH_GOOD → reward path
PATH_TIMEOUT → maximum penalty
Q3: The NOOP Quadrant
ECN/Trim + Low Delay = path problem, not load
Don't reduce CWND!
Instead: penalize path, steer traffic away
The sender has enough capacity overall
Just one path is hot → reroute
5-Step Timeline:
1. Collision on one path
2. ECN mark arrives at sender
3. Load balancer reroutes
4. If resolved → done (no CWND change)
5. If persists → delay rises → Q2 kicks in

## Slide 18
7. Parameter Scaling
Same algorithm at 100G, 400G, 800G — no retuning

## Slide 19
BDP-Ratio Scaling
Reference Network: 100 Gbps, 12 μs RTT → BDP = 150 KB
scale_a = network_BDP / reference_BDP (capacity ratio)
scale_b = target_Qdelay / reference_RTT (delay ratio)
Parameter Derivation Table
Parameter Formula 100G/12μs 400G/12μs 800G/6μs
───────────── ───────────────────────────────────────── ─────────── ─────────── ──────────
α (prop inc) 4 × MSS × scale_a × scale_b / target_Q 0.49 B/ps² 1.96 1.96
fi (fair inc) 5 × MSS × scale_a 7500 B 30000 30000
η (liveness) 0.15 × MSS × scale_a 225 B 900 900
γ (decrease) 0.8 (constant) 0.8 0.8 0.8
maxwnd 1.5 × BDP 225 KB 900 KB 450 KB

## Slide 20
8. SLEEK Loss Recovery
Why TCP's 3-DupACK fails with packet spraying

## Slide 21
SLEEK: Reordering-Tolerant Loss Detection
Problem: Spraying = Reordering
Packets take different fabric paths
Arrive out-of-order routinely
TCP: 3 out-of-order → assume loss
  With 64-way spray: nearly every ACK
  triggers false retransmission!
SLEEK Threshold
thresh = min(1.5×cwnd,
max(5×MSS, ...))
~225 OOO packets with 600KB window
vs TCP's fixed 3!
SLEEK Probe Mechanism
Explicit probes: "did you receive everything?"
Fast probe ACK → loss confirmed
Slow probe ACK → ambiguous (wait)
RTO Safety Net
min_rto = 15μs + queue_drain
× 6_hops × 8 / linkspeed
Example: 315 μs at 100G (~25× base RTT)
SLEEK is primary, RTO is backup
64-bit SACK Bitmap
Tracks 64 packets after reference seqno
Efficiently communicates gaps to sender
Much richer feedback than TCP's 3 SACK blocks

## Slide 22
9. NSCC vs TCP Cubic vs DCQCN
Three philosophies for the same problem

## Slide 23
Design Philosophy Comparison
TCP Cubic
Probe & Back Off
Increase until loss,
then cut 30%
Signal: packet loss
Shape: sawtooth
Pacing: window-based
Assumes:
• Single path
• Deep buffers
• Loss = congestion
Strengths:
• Simple, well-understood
• Works everywhere
• Self-clocking
DCQCN
Rate Staircase
ECN triggers CNP,
which steps down rate
Signal: ECN marks
Shape: staircase
Pacing: rate-based
Assumes:
• Lossless fabric (PFC)
• ECN thresholds tuned
• Timer-driven (55 μs)
Strengths:
• Hardware-friendly
• No reordering issue
• Predictable behavior
NSCC
Proportional Control
Response scales with
congestion magnitude
Signal: delay + ECN
Shape: smooth curves
Pacing: window + credit
Assumes:
• Multi-path fabric
• Shallow buffers
• Trimming available
Strengths:
• Fast convergence
• Native multi-path
• Incast-resilient (QA)

## Slide 24
10. Simulation Results
What the numbers tell us

## Slide 25
Key Simulation Findings
Fairness Convergence
8-128 NSCC flows → JFI ≈ 1.000
Converges within 5-10 RTTs
Division by cwnd ensures equal share
NSCC vs TCP Cubic Coexistence
DCQCN vs Cubic: 27%/73% (JFI=0.826)
  DCQCN too TCP-friendly
NSCC vs Cubic: 95%/5% (JFI=0.553)
  NSCC starves TCP without tuning
Key lever: qa_gate + target_Qdelay
Incast Scaling
2:1 to 128:1 incast tested
Quick-Adapt critical beyond 16:1
Without QA: completion rate drops to ~60%
With QA: completion rate stays > 98%
QA Gate Sensitivity
qa_gate=1: more aggressive → better fairness
  but higher variance across seeds
qa_gate=3: more stable throughput
  but can starve TCP in mixed traffic
qa_gate=2: recommended middle ground

## Slide 26
11. Key Takeaways
Design philosophy and lessons learned

## Slide 27
NSCC Design Principles
1
Proportional Response
Both increase and decrease scale continuously with congestion magnitude. At equilibrium, both → 0.
2
Dual-Signal Architecture
Delay provides magnitude (how bad?), ECN provides location (which path?). Together: informed decisions.
3
Steer First, Throttle Second
Q3 reroutes traffic before cutting the window. Path diversity is the first line of defense.
4
Measure Don't Guess
Quick-Adapt sets cwnd = achieved_bytes. Don't iterate toward the right answer — observe and clamp.
5
Scale by BDP Ratio
All parameters derived from reference network via scale_a/scale_b. Same algorithm at any speed.
6
Batch for Fairness
Fulfill adjustment: inc_bytes/cwnd means small windows grow faster. Converges to equal share.

## Slide 28
Anatomy of One ACK: 7 Subsystem Trace
1
ACK Arrives
Extract cum_ack, recvd_bytes, ECN echo, RTT timestamp
2
Update Flight
_in_flight -= newly_acked; _achieved_bytes += newly_acked
3
RTT Sample
raw_rtt = now − sent_time; update base_rtt if new min
4
Delay Filter
qdelay = raw_rtt − base_rtt; avg_delay EWMA update
5
Quick-Adapt?
Check 3 conditions; if all met: cwnd = achieved_bytes → return
6
Quadrant CC
Q0/Q1/Q2/Q3 based on (delay vs target) × (trim vs no-trim)
7
Fulfill?
If received > 8×MTU or time > RTT: cwnd += inc/cwnd + η

## Slide 29
When to Use NSCC (and When Not To)
NSCC Shines
Multi-path fabrics (Clos, fat-tree)
  Native spray + path steering
Shallow-buffer switches
  Proportional decrease avoids overflow
Mixed traffic patterns
  Fairness convergence via /cwnd
Incast workloads (many-to-one)
  Quick-Adapt handles 128:1
High-speed links (100G-800G)
  BDP-ratio scaling, no retuning
NSCC Struggles
Single-path networks
  No Q3 path diversity benefit
Unknown base RTT
  Bad zero-point → bad delay estimates
Very deep buffers (> 1 ms)
  Delay signal arrives too late
Coexistence with TCP (untuned)
  NSCC dominates without careful qa_gate
WAN / high-latency paths
  Designed for datacenter RTT scales

## Slide 30
Thank You
Questions & Discussion
References
UET Spec • SMaRTT-REPS • DCTCP (Alizadeh et al.) • TCP Cubic (Ha et al.)
DCQCN (Zhu et al.) • TIMELY (Mittal et al.) • Swift (Kumar et al.)
htsim2 Simulator: github.com/uet-htsim2